## Slide 1
Javier Ortiz-Tudela and Francesco Pupillo
Introduction into fMRI analysis. PsyMsc4 (Goethe 2022).
Session 1

## Slide 2
Who is this seminar for?
This is a hands-on workshop on functional Magnetic Resonance Imaging (fMRI) analysis for the PsyMSc4 at the Goethe University.
Very few assumptions are made about previous knowledge on the topic, so this workshop can be a very good entry point for complete beginners from any discipline. Also, the first introductory session could also be suited for non-scientists willing to get a broad idea into what MRI is.

## Slide 3
What is this seminar for?
The workshops will cover which are the necessary and common steps when conducting fMRI research and how to run them with MATLAB's SPM.
The core Philosophy of the workshop is that one of the main skills that a cognitive neuroscientist should have is the ability to judge what can and what cannot be done with fMRI experiments from a conceptual level. In order to acquire such a skill, one needs to understand fMRI research , i.e., to know the basics of the technique itself and the logic behind the most common analysis.

## Slide 4
How is this seminar structured?
The workshop is structured in six sessions of about 4 hours each. Each session will be dedicated to a specific processing or analysis step.
Sessions 1 - 5 will start with theory and logic behind that day's step and will continue with a hands-on exercise. Students will select a particular dataset to use for the hands-on exercises.
Session 6 will be dedicated to students' presentations. Each student will prepare a short presentation (~15 minutes / ~15 slides) describing the motivation of the study, the analysis carried out, the results obtained and their interpretation.
At the end of the workshop, each student will submit an individual brief report (2 pages max) on the results obtained with their corresponding dataset and their interpretation.
Working in groups is allowed and even encouraged. However, the individual presentations and the reports need to be unique.

## Slide 5
Part I. Basics of MRI

## Slide 6
Here are the basics of MR imaging

## Slide 7
Scanner
Coil
Bed
Here are the basics of MR imaging

## Slide 8
big and very strong!
CAUTION!!
loud and annoying!
CAUTION!!
Here are the basics of MR imaging
Scanner =
big magnet + radio frequency transmitter

## Slide 9
Scanner =
big magnet + radio frequency transmitter
MAGNETIC FIELD
When you put something inside a magnetic field, its H protons align (their spin) to the magnetic field.
Hidrogen protons
Here are the basics of MR imaging

## Slide 10
An RF pulse can tilt the orientation of the proton (‘s spin)
Hidrogen protons
Here are the basics of MR imaging
Scanner =
big magnet + radio frequency transmitter
MAGNETIC FIELD

## Slide 11
When the RF pulse stops, the protons reorient to the field emitting another RF signal.
The time taken is known as relaxation time.
Hidrogen protons
Coil =
RF receiver
Here are the basics of MR imaging
Scanner =
big magnet + radio frequency transmitter
MAGNETIC FIELD

## Slide 12
Different points in space have different relaxation times, and we can use those differences to reconstruct what is inside the scanner.
Hidrogen protons
Here are the basics of MR imaging
Scanner =
big magnet + radio frequency transmitter
MAGNETIC FIELD

## Slide 13
So… What are MR images?
If we zoom in, we can see that images are composed of pixels.
The size of each side of the pixel determines the image resolution
(1 x 1 mm, in this example).
1 mm
1 mm

## Slide 14
So… What are MR images?
Each pixel contains one value (either 1 or 0, in this example).
The current color map assigns ”black” to 0 and “white” to 1.
But remember that the color map is arbitrary!
1 mm
1 mm
0
1

## Slide 15
So… What are MR images?
1 mm
1 mm
1 mm
When we have a 3D image, we talk about voxels (1 x 1 x 1 mm, in this example).

## Slide 16
Most common 3D file formats:
NifTi (.nii)
Compressed NifTi (nii.gz)
So… What are MR images?

## Slide 17
Voxel size determines our image resolution: smaller = better.
Resolution is (partly) dependent on the strength of the magnetic field.
Common resolutions for different strengths:
1.5 Tesla ~ 3x3x3
3 Tesla ~ 2x2x2
7 Tesla ~ 0.8x0.8x.0.8
So… What are MR images?
The earth's magnetic field, at the equator, is approximately
0.00005 T

## Slide 18
- Scanner = magnet + RF transmitter
- MRI relies on the magnetic properties of the tissue.
- MR images are 3D “pictures” composed of voxels with one value per voxel.
- Most common 3D files: NifTi (.nii) and compressed NifTi (nii.gz).
- Spatial resolution depends on scanner strength.
Part I. Basics of MRI. Recap

## Slide 19
Part II. Types of MR images

## Slide 20
*For the purpose of this seminar only these two types will be covered since they are essential for standard fMRI analysis.
Anatomical images
Functional images
Types of MR images*

## Slide 21
Types of MR images
Anatomical images
(T1w)
Functional images
Aim:
Structure
Feats:
Good spatial resolution.
Task free.
Slow acquisition
(~5 min full brain)
Differences in signal strength caused by different tissue types.

## Slide 22
Aim:
Activity
Feats:
“Good” time resolution.
Measures blood flow.
Task sensitive.
Fast acquisition
(~2s full brain)
Differences in signal strength caused by distortions in the magnetic field.
Types of MR images
Anatomical images
Functional images
(T2*)

## Slide 23
Anatomical images
Functional images
How to distinguish them?
Inverse contrast!
Types of MR images

## Slide 24
Anatomical images
Functional images
How to distinguish them?
Inverse contrast!
T1w:
Grey matter – dark
White matter - bright
T2:
Grey matter – bright
White matter - dark
Types of MR images

## Slide 25
Anatomical images
Functional images
How to distinguish them?
Functional images have (usually) lower spatial resolution.
Gain in time resolution!
time
Types of MR images

## Slide 26
Anatomical images
Functional images
How to distinguish them?
TR = time to sample the entire field (to collect one brain volume).
time
TR
TR
TR
TR
TR
TR
TR
TR
TR
TR
TR
TR
Types of MR images

## Slide 27
Functional runs. What are they?
Noise due to scanner drift accumulates over time so collecting images for too long will cause your images to look bad.
Solution: divide your task into shorter blocks, i.e., runs.
Aprox. run duration: ~10 minutes (adults) / ~6 minutes (children).
Max duration: 15 minutes (ideally shorter).
Run duration is often measured in volumes.
time
TR
TR
TR
TR
TR
TR
TR
TR
TR
TR
TR
TR
Types of MR images. Functional images

## Slide 28
Part II. MR images types. Recap
Key ideas.
MR images can be roughly grouped into anatomical and functional images.
Anatomical images (usually one volume) have higher spatial resolution than functional images (usually several volumes).
TR = time to collect one brain volume.
Runs = blocks of recording time.

## Slide 29
Part III. Image preprocessing

## Slide 30
Preprocessing.
Why?
MR images as a reconstruction problem > This process is never perfect.
Distortions in MR images can be grouped in two types: temporal and spatial.

## Slide 31
Why?
MR images as a reconstruction problem > This process is never perfect.
Distortions in MR images can be grouped in two types: temporal and spatial.
If collecting this entire volume takes 2s (TR=2s), it means that the top slice was acquired ~2 after the bottom one!
Acquisition order
0s
TRs
Preprocessing.

## Slide 32
Why?
MR images as a reconstruction problem > This process is never perfect.
Distortions in MR images can be grouped in two types: temporal and spatial.
Acquisition order
If collecting this entire volume takes 2s (TR=2s), it means that the bottom slice was acquired ~2 after the top one!
0s
TRs
Time
0s
TRs
Preprocessing.

## Slide 33
Acquisition order
Slice time correction
0s
TRs
Time
0s
TRs
Why?
MR images as a reconstruction problem > This process is never perfect.
Distortions in MR images can be grouped in two types: temporal and spatial.
Preprocessing.

## Slide 34
Why?
MR images as a reconstruction problem > This process is never perfect.
Distortions in MR images can be grouped in two types: temporal and spatial.
Magnetic field inhomogeneities
“Magnetic field inhomogeneities, caused by susceptibility differences at tissue/air and tissue/bone interfaces, result in significant geometric and intensity distortions. The challenge of reducing these field inhomogeneity effects arises from their spatial dependence. Data from different spatial locations are corrupted to different degrees, with the amount of corruption determined by the local magnetic field environment.” (Gholipour, et al., 2011).
Preprocessing.
Notes: 34

## Slide 35
While some minor field inhomogeneity can be corrected by (automatic) shimming, much of it cannot…
Two main approaches to tackle the resulting distortions:
- Field map, i.e., acquiring a map of the magnetic field
- Blip up – blip down, i.e., acquiring an image in the inverted phase - encoding direction (Holland, Kuperman, & Dale, (2010).
Why?
MR images as a reconstruction problem > This process is never perfect.
Distortions in MR images can be grouped in two types: temporal and spatial.
Magnetic field inhomogeneities
Preprocessing.
Notes: 35

## Slide 36
Why?
MR images as a reconstruction problem > This process is never perfect.
Distortions in MR images can be grouped in two types: temporal and spatial.
Intensity inhomogeneities
Preprocessing.
Notes: 36

## Slide 37
Why?
Functional MR images are recorded over time > Participants move!
Volumes need to be re-aligned!
Preprocessing.
Notes: 37

## Slide 38
Why?
Anatomical and functional MR images are recorded at different time points and with different sequences > Volumes need to be registered to each other!
Preprocessing.
Notes: 38

## Slide 39
Why?
MR images are recorded for multiple individuals > Participants have different brain shapes!
We might want to have a common space for all of them.
Preprocessing.
Notes: 39

## Slide 40
Why?
MR images are recorded for multiple individuals > Participants have different brain shapes!
Preprocessing.
Common spaces:
Native
MNI
Sample specific
Notes: 40

## Slide 41
Key steps.
- Slice-time correction
- Magnetic field distortions
- Intensity inhomogeneities
- Motion correction
- Registration
- Normalization
Part III. Image preprocessing. Recap
Notes: 41

## Slide 42
How to run fMRIPrep on your own:https://gitlab.com/ortizTud/neuroim-methods#010321-tutorial-on-fmriprep-ortiz
How to do this?
- fMRIprep (https://fmriprep.org)
- SPM
- FSL
- BrainVoyager
- … and more
Key steps.
- Slice-time correction
- Magnetic field distortions
- Intensity inhomogeneities
- Motion correction
- Registration
- Normalization
Part III. Image preprocessing. Recap
Notes: 42

## Slide 43
Let’s get practical.
Software needed:
MATLAB 2018 or later (https://www.mathworks.com/)
SPM12 (https://www.fil.ion.ucl.ac.uk/spm/software/spm12/)
ITK-Snap 3.8.0 (http://www.itksnap.org/)
Data needed:
Know our repository:
https://github.com/ortiztud/fmri_analysis_intro
All the steps involved in preprocessing take a while to complete (up to several hours sometimes!)
We have already preprocessed all the images with fMRIPrep. You can find them under
~/<project_folder>/preproc_data/fmriprep/
Notes: 43